## Slide 1: A Randomized Trial of Continuous Noninvasive Blood Pressure Monitoring During Noncardiac Surgery
R2สุพฤกษ์ /อ.ณัฐธพงษ์

## Slide 2: Introduction
Intraoperative hypotension is strongly associated with postoperative mortality
Notes: Intraoperative hypotension is strongly associated with postoperative mortality. For example, hypotension was the most important factor responsible for postoperative mortality in the Perioperative Ischemia
Evaluation Trial.1 Many other studies similarly report strong associations between hypotension and postoperative acute kidney injury (AKI) and myocardial injury

## Slide 3: Introduction

## Slide 4: Introduction
Optimizing intraoperative hemodynamics and avoiding hypotension may reduce perioperative myocardial and renal injury

## Slide 5: Introduction
Intraoperative hypotension has various definitions
Mean arterial pressure (MAP) <65 mm Hg has been associated with worse outcomes

## Slide 6: Introduction
Intraoperative blood pressure : noninvasive oscillometric devices every 3–5 minutes

## Slide 7: Introduction
An alternative is noninvasive finger cuff monitoring which can provide continuous hemodynamic monitoring
The system provides continuous beat-to-beat blood pressure, along with stroke volume, stroke volume variation, cardiac output, and systemic vascular resistance

## Slide 8: Introduction
The ClearSight (Edwards Lifesciences Corp, Irvine, CA)

## Slide 9: Introduction
Hypothesis :
Continuous noninvasive monitoring of blood pressure in moderate-to-high-risk surgical patients reduces the duration and severity of intraoperative hypotension compared to intermittent NIBP

## Slide 10: Methods
Study was approved by the Cleveland Clinic Institutional Review Board
Informed consent from all subjects participants
The trial was registered at clinicaltrials.gov

## Slide 11: Methods
enrolled 320 adults
Inclusion criteria :
45 years or older
ASA III or IV
noncardiac surgery with general anesthesia
Notes: is a continuous noninvasive hemodynamic monitor which uses volume clamp and physiocal methods.1

## Slide 12: Methods
Exclusion criteria :
  Invasive arterial monitoring was needed (by anesthesiologist)
  >10% discrepancy in preoperative MAP between arms
  The expected duration of surgery was <2 hours

## Slide 13: Methods
Patients were randomly allocated to continuous unblinded or blinded continuous monitoring by an investigator not involved in clinical care
1:1 ratio, computer-generated random number via a web-based system (REDCap secure web application)

## Slide 14: Methods
The continuous monitor was placed on all patients in addition to the intermittent oscillometric cuff on opposite arms

## Slide 15: Methods
continuous monitoring group
  Information from the continuous monitor was available to the clinicians in addition to the usual oscillometric values
blinded group
  blood pressure management was based only on intermittent oscillometric BP monitoring
  the information from continuous monitors was not available to the clinicians but recorded for analysis purposes

## Slide 16: Methods
Induction in all patients
  Standard monitoring
  etomidate (0.2–0.3 mg/kg) or propofol (1–2 mg/kg)
  vecuronium (0.1 mg/kg) or rocuronium (0.6 mg/kg)
  fentanyl (1–2 μg/kg)
Notes: (electrocardiography, noninvasive blood pressure, oxygen saturation, temperature

## Slide 17: Methods
in all patients
Inhalation anesthetics (up to 1.5 MAC)
50%–80% inspired oxygen and air

## Slide 18: Methods
Clinicians were thus free to use
  type and amount of intravenous fluids
  dose of vasopressors and inotropes
  adjust the inhalational concentration
  intravenous anesthetic drugs

## Slide 19: Methods
TWA MAP under a threshold of 65 mm Hg was calculated as the area between 65 mm Hg threshold and the curve of the MAP measurements divided by total continuous reading time:
Notes: TWA is similar to an ordinary arithmetic mean, except that instead of each of the MAP measures contributing equally to the final average, some MAP measures contributed more than others

## Slide 21: Methods
AKI
AKIN classification, modified per Walsh to exclude urine output
We also extended the normal 48-hour creatinine window used in the AKIN criteria to 7 days to better characterize the postoperative period

## Slide 22: Methods
Quality of recovery (QOR-15) and postoperative morbidity survey (POMS)
  on the third postoperative day or at discharge
Notes: based on which occurrence came first, by a blinded research fellow

## Slide 23: Methods
Quality of recovery (QOR) :
  emotional state
  physical discomfort
  psychological support
  physical independence
  pain

## Slide 24: Methods
Postoperative morbidity survey (POMS) :
  18-item survey that addresses 9 domains of postoperative morbidity
  reliable and valid descriptor of short-term postoperative morbidity

## Slide 25: Statistical Analysis
For primary analysis, 2 randomized groups were compared on the TWA MAP <65 mm Hg
2-sample Wilcoxon rank-sum test and Hodges Lehmann estimation of location shift with corresponding asymptotic 95% CI
the primary result was adjusted for slightly imbalanced age and type of surgery via multivariable generalized linear model with logit link function

## Slide 26: Statistical Analysis
2 secondary analyses, in which the outcomes TWA MAP under MAP <60 mm Hg
and MAP <55 mm Hg

## Slide 27: Statistical Analysis
Six exploratory outcomes including
  transfusion requirement
  AKI
  in-hospital composite of death,stroke, or myocardial injury after noncardiac surgery
  QOR score
  POMS
  hospital lengths

## Slide 28: Results

## Slide 29: Results

## Slide 30: Results

## Slide 31: Results

## Slide 32: Results

## Slide 33: Results

## Slide 34: Discussion
Continuous noninvasive blood pressure monitoring in moderate-to-high-risk surgical patients reduced the duration and severity of hypotension
The median time spent <65 mm Hg was nearly halved (2 vs 4 minutes)
in the continuous monitoring group
Notes: although we did not formally compare the 2 groups on duration of hypotension outcome

## Slide 35: Discussion
The amounts of hypotension were also lower under thresholds of 60 and 55 mm Hg in the continuous monitoring group
The differences in TWA MAP are relatively small but even few minutes
of extra hypotension is associated with worse outcome
Notes: For example, just a single minute at a MAP of 50 mm Hg
increases the risk of mortality 5%.10

## Slide 36: Discussion
The results are consistent with Meidert et al
Randomized 160 orthopedic surgery patients to continuous blood pressure monitoring or monitoring every 3 minutes
continuous monitoring improved hemodynamic stability
Notes: However, Meidert et al18 used the oscillometric blood pressure values every 3 minutes for the first hour of general anesthesia; in contrast, we compared continuous blood pressure measurements every 20 seconds
throughout surgery.

## Slide 37: Discussion
The TWA <65 of 0.11 mm Hg in the oscillometric group means that the average patient had an exposure 0.11 mm Hg below 65 mm Hg throughout surgery.
With an average case duration in the study of nearly 4 hours, a TWA MAP of 0.11 corresponds to 0.11 mm Hg times 240 minutes = 26 mm Hg ×minutes.
In this example, 26 mm Hg x minutes could refer to a patient who spent 13 minutes at 63 mm Hg or approximately 4 minutes at 59 mm Hg

## Slide 38: Discussion
Once hypotension is detected, the optimal treatment is often unclear and depends on numerous factors
Advanced hemodynamic parameters can guide management of hypotension

## Slide 39: Discussion
The impact of continuous monitoring may have been limited by lack of set protocol for hypotension management
Clinicians may also have mistrusted the accuracy of ClearSight blood pressure and ancillary measurements, despite good validation

## Slide 40: Discussion
In summary, continuous noninvasive blood pressure monitoring nearly halved the amount of intraoperative hypotension in adults having noncardiac surgery
Because continuous monitoring allowed clinicians to detect hypotension earlier and respond effectively

## Slide 41: Discussion
Avoiding hypotension may well reduce the incidence of serious complications

## Slide 42: Critical Appraisal
Does this study address a clear question?

## Slide 43: Critical Appraisal
Are the results of this single trial valid?
Notes: คิดตามสิ่งที่เราตั้งใจจะให้เขาทำตั้งแต่แรก ก็คือไม่ว่าคุณจะเอายากลับไปกินหรือไม่กิน เราก็จะถือว่าคุณอยู่ในกลุ่มยา เรียกว่าแบบ intention-to-treat
ข้อที่ดีกว่าเป็นอย่างมากของแบบที่สองนี้คือว่ามันยังรักษาความที่มันเกลี่ย ลักษณะที่เรา random ไว้ตั้งแต่แรกไว้ด้วยครับ ดังนั้นหากไม่มี intention to treat แล้วจริงๆ ก็ไม่รู้ว่าจะ randomize ไปทำไม ทำให้ขาดความน่าเชื่อถือไปเป็นอย่างมากครับ ซึ่งโดยส่วนใหญ่เดี๋ยวนี้ผู้วิจัยก็รู้กันและจะทำการวิเคราะห์แบบ intention-to-treat อยู่แล้ว ยกเว้นผู้วิจัยกลุ่มเล็กๆ ที่ยังไม่เคยรู้จัก EBM ครับ

## Slide 44: Critical Appraisal
Are the results of this single trial valid?

## Slide 45: Critical Appraisal
-
Yes
0.05 [0.00, 0.22]vs 0.11 [0.00, 0.54]
P value = 0.039
Notes: Primary outcome
TWA MAP <65 mm Hg (mm Hg)

## Slide 46: Critical Appraisal : RCT
Can I apply these valid, important results to my patients?